## Slide 1: Changes since Last Rev
Made detector FWHM change as a function of energy (link to Mirion)

## Slide 2: Known Inaccuracies
Description | Possible Fix | Affects proton gated spectrum?
All x-rays emitted are k-alpha1 for both internal conversion and electron capture | Incorporate all possible x-ray energies and corresponding probabilities | Yes
All electrons emitted by internal conversion are from lowest energy level | Include non-zero probability for higher energy electrons | Only when accidental coincidences occur (not currently simulated)
No modeling of auger electrons | TBD | Yes, but likely small effect
Beta spectrum is uniform | Use BetaShape program | Yes, but effect is small because beta background is small
x-ray peak from IC in coincidence with EC (see following slide) | Disallow internal conversion following electron capture? Or reduce it’s probability? | Only when accidental coincidences occur
Does not include further decays of 73Br, 72Se, etc | Add these decays in | Only when accidental coincidences occur

## Slide 3: 500 mm^2 LEGE, 73KR, Full Spectrum, no dead layer
K-alpha X-ray
peaks of Br, mostly from I.C.
73Br gamma rays
23.8keV from IC&EC x-ray in coincidence (maybe not physical, see dedicated slide)
IC x-rays in coincidence with gamma ray

## Slide 4: 500 mm^2 LEGE, 73KR, Full Spectrum, with

## Slide 5: 500 mm^2 LEGE, 73KR, No Beta+ Background, Full Spectrum

## Slide 6: Ortec GLP 500 mm^2 x 13 mm, full spectrum, no dead layer

## Slide 7: 23.8 keV Peak
The 26.8 keV state of 73Br almost always undergoes internal conversion when it transitions to the ground state, so most EC to an excited state which passes through the 26.8 keV state will emit a second x-ray. In reality this peak may not be present or be much smaller because of the electron destroyed by EC.

## Slide 8: 500 mm^2 LEGE, 73KR, channels that don’t emit a proton disabled, no dead layer
Br K-alpha
Se K-alpha

## Slide 9: 500 mm^2 LEGE, 73KR, channels that don’t emit a proton disabled, with dead layer

## Slide 10: 500 mm^2 LEGE, 73KR, channels that don’t emit a proton disabled, no dead layer

## Slide 11: 500 mm^2 LEGE, 73KR, channels that don’t emit a proton disabled, with dead layer

## Slide 12: Ortec GLP 500 mm^2 x 13 mm, channels that don’t emit a proton disabled, no dead layer
Trough is about 2x higher than for LEGe

## Slide 13: Ortec GLP 500 mm^2 x 13 mm, channels that don’t emit a proton disabled

## Slide 14: 1 hr of run time
Assume use beam for 30% of the time
Use stopped beam rate for PAC2 and 73Kr => 3.7e6 pps
  accidental coincidences seem likely here…
Proton branching ratio = 2.5e-3
Assume 10% efficient at detecting protons
Detected events per day ~1e6 events per hour

## Slide 15: 500 mm^2 LEGE, 73KR, channels that don’t emit a proton disabled, 1hr of PACII

## Slide 16: 500 mm^2 LEGE, 73KR, channels that don’t emit a proton disabled, 1hr of PACII

## Slide 17: Next Steps
Try gating on detlaE & E
Make decay schemes for other isotopes
  Which one first?
Anything that should be improved for better accuracy?